## Slide 1: Cadence Tips & Tricks
Alicia KLINEFELTER
ECE 3663, Spring 2013

## Slide 2: Outline
Using NXClient for Cadence
Cadence Setup
Schematic Labels
Exporting plots for presentations/papers/homework
Presenting schematics
Using Open Command Environment for Analysis (OCEAN) for simulation
Monte Carlo simulations (MCS) in FreePDK

## Slide 3: Using NX Client from Home
Schematic viewer (Virtuoso) is incredibly slow from home.
Use the following NXClient settings from home to speed up your work.
  Under the advanced tab
    Select “Disable DirectDraw for screen rendering”
    Under “Cache” max out both dropdowns
max out
cache

## Slide 4: Helpful Cadence Setup
Set up Cadence in two commands
Set environment variables in ~/.bashrc file to jump to Cadence run directory:
  export FREEPDK=/homenfs/platou/<userID>/cadence/freePDK/
Use bash script to run all setup commands
  Script provided on Wiki

## Slide 5: Adding Schematic Labels
Schematic labels help in many scenarios
  Visual complexity of design (too many wires!)
  Automatic names for plotted signals
    No “/net3” voltage signals in plots
  Act as documentation
same net

## Slide 6: How To Add Schematic Labels
Create  Wire name…
  Hotkey: L
ADD MULTIPLE NET NAMES (SPACE DELIMITED)
  “Hide” and then select nets to drop label names

## Slide 7: Exporting Plots
Black plot backgrounds are not ideal
  Plots will be difficult to see in presentations
  You will hemorrhage through your black ink cartridge printing out one homework
Options
  Modify plots in Cadence
  Export data, plot within MATLAB/Python/Excel/etc.
  Screenshots are technically an option, but it’s not the best practice


## Slide 8: Modify Plots in Cadence
AXIS  STRIPS
GRAPH  EDIT…
  To modify color scheme
  This is a visual/optional step, to get trace color correct

## Slide 9: Modify Plots in Cadence
DOUBLE CLICK ON TRACES
FILE  SAVE AS IMAGE…
  Check box for “Use white background”!

## Slide 10: Export Plot Data
RIGHT-CLICK ON TRACE  SAVE
Can export to csv, matlab formats

## Slide 11: White Background for Schematics
Black schematic backgrounds are not a good idea
  Presentation visibility
  Printing many of these will be bad for ink
    Depending on the printer, it may not even show up
  Example schematic to the right is bad, but it gets worse with complicated designs
From schematic viewer window: File Export Image

## Slide 12: OCEAN for Simulations
Lets you setup, simulate, and analyze circuit data
  Simulation programming language
  Good for repetitive tasks
  Built-in calculator
  Run longer analyses such as parametric analyses, Corners Analyses, and statistical analyses more effectively
  Run simulations from a non-graphic, remote terminal
OCEAN tutorial on Wiki
  venividiwiki.ee.virginia.edu/mediawiki/index.php/ToolsCadenceTutorialsBasicSimulationOceanFreePDK
OCEAN documentation on server
  /net/plato.ee.virginia.edu/app/cadence/ic/doc/oceanref
  Google-ing for OCEAN help isn’t helpful

## Slide 13: Getting Example OCEAN Script
Making script from scratch is annoying
Use ADE to create one
  Within ADE: Session  Save Ocean Script…
  Exports your current simulation settings
simulator( 'spectre )
design( "/net/plato.ee.Virginia.EDU/users/amk5vx/simulation/fo4_inverter/spectre/schematic/netlist/netlist")
resultsDir( "/net/plato.ee.Virginia.EDU/users/amk5vx/simulation/fo4_inverter/spectre/schematic" )
modelFile(
'("/net/plato.ee.virginia.edu/app/lib/freepdk45/trunk/ncsu_basekit/models/hspice/tran_models/models_nom/NMOS_VTL.inc" "")
'("/net/plato.ee.virginia.edu/app/lib/freepdk45/trunk/ncsu_basekit/models/hspice/tran_models/models_nom/PMOS_VTL.inc" "")
'("/net/plato.ee.virginia.edu/app/lib/freepdk45/trunk/ncsu_basekit/models/hspice/tran_models/models_nom/NMOS_VTG.inc" "")
'("/net/plato.ee.virginia.edu/app/lib/freepdk45/trunk/ncsu_basekit/models/hspice/tran_models/models_nom/PMOS_VTG.inc" "")
)
analysis('tran ?stop "15u" ?errpreset "moderate" )
desVar( "vdd" 1.2 )
save( 'v "/dut_in" "/orig_pulse" "/dut_out" "/x4_inv_out" )
save( 'i "/V0/MINUS" )
temp( 27 )
run()
selectResult( 'tran )
plot(getData("/dut_in") getData("/orig_pulse") getData("/dut_out") getData("/x4_inv_out") getData("/V0/MINUS") )

## Slide 14: Useful OCEAN Functions
VDDLIST = list(0.3 0.4 0.5 0.6 0.7 0.8)
foreach( VDD VDDLIST
of = outfile("~/Results/fo4_inv/output.txt" "a")
desVar( "vdd" VDD )
vdd = VDD
option( 'dochecklimit "no"
)
Looping structures
  foreach()
  while()
Conditionals
  if()
  case()
;; Length of all devices in circuit
desVar( "length" 50n )
;; Width of the n/p devices
desVar( "n_width" 90n )
desVar( "p_width" 180n )
length=50n
n_width=90n
p_width=180n
Setting variables to use in the netlist
subckt INVX16TS A VDD VSS Y
NMOS (Y A VSS VSS) NMOS_VTH w=16*n_width l=length
PMOS (VDD A Y VDD) PMOS_VTH w=16*p_width l=length
ends INVX16TS

## Slide 15: Useful OCEAN Functions
of = outfile("~/Results/fo4_inv/output.txt" "a")
fprintf( of "VDD(V) Delay(s)\n")
<RUN ANALYSIS>
diff = abs((cross(v("in") vdd/2 1 "either" nil nil) - cross(v("out") vdd/2 1 "either" nil nil)))
plot( diff ?expr '( "diff" ) )
fprintf( of "%g %g\n", vdd, diff)
close(of)
File I/O
  Formatting similar to C
Calculator functions
  Same syntax
Plotting

## Slide 16: Running the Script
For circuit simulations, create directory with:
  OCEAN script
  Stimuli file (if applicable)
  Circuit netlist
  Netlist footer
  Netlist header
If simulation was run in ADE, the netlist and _graphical_stimuli.scs file are located:
  /simulation/<design name>/spectre/schematic/netlist/
[amk5vx@class4 mc_test]$ . cadence2011
... Cadence environment is set up.
Documents are under /app/cadence/*/doc, the html index file usually ends with '*TOC.html'.
[amk5vx@class4 mc_test]$ ocean
…
ocean> load "ocnScript.ocn"

## Slide 17: OCEAN for Max Frequency
Requires iteration, binary search
  Tedious to do in ADE with high granularity
Pseudo-code assuming the output value is known?
  for {all frequencies in range}
    Run transient simulation at frequency x
    Check output values
    If they are correct, circuit success!
    Else, the circuit failed at this frequency. Fail!
    Print to the console the last successful frequency
Express this in OCEAN syntax!
  Start iterating lowest frequency first
    Check for existence before doing math: if (t1 && t2 && t3)
      OCEAN errors out when doing math on “nil” data type
ALU
opCode
in1
in2
out0
out1
clk

## Slide 18: OCEAN for Power Determination
Many methods for computing circuit power
  pavg=(iavg over 1 clock period)*v
Measuring current can be tricky
  Many transistor symbols wont let you measure current using their terminals
  You can put in a “dummy” voltage source (0V) for measurement
    All components found in the library analogLib
Determining power across frequencies
  Can use Cadence calculator, but tedious for so many frequencies
  How can you incorporate this into your OCEAN script?
measuring current

## Slide 19: Monte Carlo Simulation
Transistor properties vary from wafer to wafer
  Process variations (VT)
  Lithography (W, L, wire width)
Transistor model parameters are averages
  Parameters are more distributed in silicon
Monte Carlo simulates circuit over range of values for device parameters
{W, L, VT}
{Delay, Sensitivity}

## Slide 20: Monte Carlo Simulation
;; Now we need to define the models for the transistors
;; Here we hardcode the path to the model library
;; DEFINE THE MODEL
libdir = "./freepdk.scs" ; LIBRARY PATH
;; Set parameters specific to this model library to select the right model
deviceOption = "lvt"
Corner = "SS" ; "TT" "FS" "FF" "SF" "SS" = THE GLOBAL CORNER CASES
…
;; RUN THE SIMULATION
monteCarlo( ?numIters 10 ?analysisVariation 'processAndMismatch ?sweptParam "None" ?sweptParamVals "25" ?saveData t )
;; MONTE CARLO EXPRESSION FOR MEASUREMENTS (Remember to put the monteexpr's BEFORE the monterun.
;; Or else the expression values would not get printed in the mcdata file)
monteExpr( "rt" "riseTime(v(\"out\" ?result 'tran) 0.5n t 1.5n t 10 90)" )
monteExpr( "ft" "riseTime(v(\"out\" ?result 'tran) 1.5n t 2.5n t 10 90)" )
;; START MONTE CARLO SIMULATION
save( 'all )
resultsDir("mcPSF")
monteRun()
…

## Slide 21: Provided Files and Descriptions
For running Cadence using the bash script:
  run_cadence.sh
Example OCEAN scripts:
  monteCarlo.ocn / netlist